## Slide 1: RISC vs. CISC

## Slide 2: RISC vs. CISC
ISA
  Instruction set architecture
    Instructions supported by a particular processor
    Their byte-level encodings
CISC
  Complex instruction set computer
RISC
  Reduced instruction set computer

## Slide 3: CISC
Involved from the earliest computers
Mainframe and Minicomputers
  By the early 1980s
  their instruction sets had grown quite large
    Manipulating circular buffers
    performing decimal arithmetic
    evaluating polynomials
Microcomputer
  Appeared in 1970s, had limited instruction sets
    constrained by number of transistors on a single chip
  By the early 1980s, followed the path to increase their instruction sets

## Slide 4: RISC
Developed in the early 1980s
  philosophy
    One are able to generate efficient code for a simpler form of instruction set
    Complex instructions are hard to generated with a compiler and seldom used
John Cocke (1925-2002)
  1987 ACM Turing Award
David Patterson(UC Berkeley), John Hennessy (Stanford U)
  2017 ACM Turing Award

## Slide 5: RISC
IBM | Power
IBM and Motorola | PowerPC
Sun Microsystems | SPARC
Digital Equipment Corporation | Alpha
Hewlett Pack | Pa-risc
MIPS Technologies | MIPS
Acorn Computers Ltd | ARM(Acorn RISC Machine)

## Slide 6: RISC vs. CISC
CICS | Early RISC
A large number of instructions | Many fewer instructions (<100)
Some instructions with long execution times | No instruction with a long execution time
Variable-length encodings. (x86-64 1~15 bytes) | Fixed-length encodings
Multiple formats for specifying operands | Simple addressing formats
Arithmetic and logical operations can be applied to both memory and register operands | Arithmetic and logical operations only use register operands. load/store Architecture

## Slide 7: RISC vs. CISC
CICS | Early RISC
Implementation artifacts hidden from machine level programs | Implementation artifacts exposed to machine level programs
Condition codes | explicit test instructions store the test results in normal registers for use in conditional evaluation
Stack-intensive procedure linkage | Registers are used for procedure arguments and return addresses

## Slide 8: RISC
Cons for early RISC
  More instructions
  Not multiple cycles
  Exposing implementation artifacts to machine level programs
Pros for RISC
  Well suited for pipeline (high efficient implementation)

## Slide 9: Y86-64
The Y86-64 instruction set
  Includes attributes of both CISC and RISC
  Can be viewed as taking a CISC instruction set (x86-64) and simplifying it by applying some of the principles of RISC
On the CISC side
  condition codes, variable-length instructions
  uses the stack to store return addresses.
On the RISC side,
  a load/store architecture
  a regular instruction encoding
  passes procedure arguments through registers

## Slide 10: RISC vs. CISC
In the early 1990s, the debate diminished
  neither RISC nor CISC in their purest forms are better than designs that incorporated the best ideas of both

## Slide 11: RISC
Evolved and introduced more instructions
  many of which take multiple cycles to execute
  Have hundreds of instructions
Exposing implementation artifacts to machine-level programs
  proved to be shortsighted
  As new processor models were developed
    using more advanced hardware structures,
    many of these artifacts became irrelevant,
    but they still remained part of the instruction set

## Slide 12: CISC
The core of RISC design
  is well suited to execution on a pipelined machine
X86 incorporates RISC features
  Dynamic translating CISC instructions to RISC-like ops and taking pipeline architectures
  X86-64 introduces more RISC features

## Slide 13: CISC
Marketing issues determine the success of the ISAs
  X86 wins in high-end server, desktop, laptop machines
  RISC win in market of embedded processors and the smart phones

## Slide 14: CISC
Intel made it easy to keep moving from one generation of processor to the next
  By maintaining compatibility with its existing processors
As integrated-circuit technology improved
  x86 processor manufacturers could overcome the inefficiencies created by the original 8086 instruction set design
  using RISC techniques to produce performance comparable to the best RISC machines.

## Slide 15: RISC
RISC processors have done very well in the market for embedded processors
In these applications, saving on cost and power is more important than maintaining backward compatibility
  In terms of the number of processors sold
this is a very large and growing market

## Slide 16: Logical Design & HCL

## Slide 17: Topics
Logic design
Hardware Control Language HCL
Suggested Reading: 4.2

## Slide 18: Logic Design
Digital circuit
  What is digital circuit?
  Know what a CPU will base on?
Hardware Control Language (HCL)
  A simple and functional language to describe our CPU implementation
  Syntax like C

## Slide 19: Category of Circuit
Analog Circuit
  Use all the range of Signal
  Most part is amplifier
  Hard to model and automatic design
  Use transistor and capacitance as basis
  We will not discuss it here
Voltage
Time

## Slide 20: Category of Circuit
Digital Circuit
  Has only two values, 0 and 1
  The voltage of 1 is differ in different kind circuit.
    E.g. TTL circuit using 5 voltage as 1
  Use voltage thresholds to extract discrete values from continuous signal
Voltage
Time
0
1
0

## Slide 21: Digital Signals
Digital Circuit (cont.)
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
  Easy to model and design
  Use true table and other tools to analyze
  Use gate as the basis

## Slide 22: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Not an assignment operation, just give the circuit a name
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay
a
b
out
a
b
out
a
out
out = a && b
out = a || b
out = !a
And
Or
Not

## Slide 23: Overview of Logic Design
Electronic circuits are used to
  Compute functions on bits (computational logic)
  Store bits in different kind of memory elements (memory elements)
Clock Signals
  Are used to regulate updating of the memory elements
    Clock : a periodic signal
Rising
edge
falling
edge

## Slide 24: Combinational Circuits

## Slide 25: Combinational Circuits
Acyclic Network of Logic Gates
  Continuously responds to changes on inputs
  Outputs become (after some delay) Boolean functions of inputs
Acyclic Network
Inputs
Outputs

## Slide 26: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 27: Hardware Description Language
Once designers created circuit designs by
  drawing schematic diagrams of logic circuits
    first with paper and pencil
    later with computer graphics terminals
Now most designs are expressed in a HDL
  a textual notation that looks similar to a programming language
    that is used to describe hardware structures rather than program behaviors

## Slide 28: Hardware Description Language
The most commonly used languages are
  Verilog, having a syntax similar to C
  VHDL, having a syntax similar to the Ada
These languages were originally designed
  For creating simulation models of digital circuits
Logic synthesis programs were created
  that could generate efficient circuit designs from HDL descriptions
  in the mid-1980s

## Slide 29: Hardware Description Language
There are now a number of commercial synthesis programs
  Logic synthesis has become the dominant technique for generating digital circuits
Similar shifts
  from hand-designed circuits to synthesized
  from assembly programming to high-level language programming

## Slide 30: Hardware Control Language
A language to describe
  the control logic of the different processor designs
The control logic
  is the most difficult part of designing a microprocessor
Carefully separating out, designing, and testing the control logic
  we can create a working microprocessor with reasonable effort
There are tools that can directly translate HCL into Verilog

## Slide 31: Practice Problems
Write an HCL expression for a signal xor
  equal to the exclusive-or of inputs a and b.
What is the relation
  between the signals xor and eq ?

## Slide 32: Word Equality
  64-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
=
B
A
eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
eq

## Slide 33: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
  Its name: MUX
  Usage: Select one signal from a couple of signals
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 34: Word Multiplexor
Word-Level Representation
s
B
A
Out
MUX
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
HCL Representation ?

## Slide 35: Word Multiplexor
HCL Representation
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs (Don’t require mutually)
    Output value for first successful test
Out = [
s : A;
1 : B;
];
default case
!s

## Slide 36: HCL Word-Level Examples
Find minimum of three input words
HCL case expression
Final case guarantees match
A
Min3
MIN3
B
C
word Min3 = [
A < B && A < C : A;
B < A && B < C : B;
1 : C;
];
Minimum of 3 Words
HCL Representation
Notes: 好像这个Min可以简化的。求B时，条件可以为：B<C

## Slide 37: Practice Problems
The HCL code given for computing the minimum of three words contains
  four comparison expressions of the form X <= Y
Rewrite the code to compute the same result
  but using only three comparisons

## Slide 38: HCL Word-Level Examples
D0
D3
Out4
s0
s1
MUX4
D2
D1
Select one of 4 inputs based on two control bits
HCL case expression
Simplify tests by assuming sequential matching
word Out4 = [
!s1&&!s0: D0;
!s1 : D1;
!s0 : D2;
1 : D3;
];
4-Way Multiplexor
HCL Representation
Notes: 好像这个Min可以简化的。求B时，条件可以为：B<C

## Slide 39: Arithmetic Logic Unit
OF
ZF
SF
OF
ZF
SF
OF
ZF
SF
OF
ZF
SF
Combinational logic
  Continuously responding to inputs
Control signal selects function computed
  Corresponding to 4 arithmetic/logical operations in Y86
Also computes values for condition codes
We will use it as a basic component for our CPU
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 40: Storage (Sequential Circuits)

## Slide 41: Storage (Clocked Registers)
Clocked Registers
  e.g. Program Counter(PC), Condition Codes(CC)
  Hold single words or bits
  Loaded as clock rises
  Not “program registers”
Clock
  determines when new values are to be loaded into the devices
I
O
Clock
Clock
Rising
edge
falling
edge

## Slide 42: Register Operation
Stores data bits
For most of time acts as barrier between input and output
As clock rises, loads input
State = x
Rising
clock
Output = x
Input = y
x
State = y
Output = y
y

## Slide 43: State Machine Example
0
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load

## Slide 44: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
?
X0
X0
?
1
X0

## Slide 45: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X0
X0+X0
0
X0
X0
X0
X0

## Slide 46: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X1
X0+X1
0
X0
X0
X0
X0
X1

## Slide 47: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X1
X0+X1+X1
0
X0
X0
X1
X0+X1
X0+X1
X0+X1

## Slide 48: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X2
X0+X1+X2
0
X0
X0
X1
X0+X1
X0+X1
X0+X1
X2

## Slide 49: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X2
X0…X2
0
X0
X0
X1
X0+X1
X0…X2
X0…X2
X2
X0…X2

## Slide 50: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X3
X3
1
X0
X0
X1
X0+X1
X0…X2
X0…X2
X2
X0…X2
X3

## Slide 51: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X3
X3
1
X0
X0
X1
X0+X1
X3
X3
X2
X0…X2
X3
X3

## Slide 52: State Machine Example
0
Clock
Load
In
Out
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
X0
X0
X1
Accumulator circuit
Load or accumulate on each cycle
X2
X3
X4
X5
X0+X1
X0…X2
X3
X3+X4
X3…X5

## Slide 53: Storage (Random-access memories)
Random-access memories
  e.g. Register File, Memory
  Hold multiple words
    Address input specifies which word to read or write
  Possible multiple read or write ports
  Read word when address input changes
  Write word as clock rises

## Slide 54: Register File
Register file
  Holds values of program registers
  %rax, %rsp, etc.
  Register identifier serves as address
    ID “F” implies no read or write performed
Multiple Ports
  Can read and/or write multiple words in one cycle
    Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 55: Register File Timing
Reading
  Like combinational logic
  Output data generated based on input address (After some delay)
Writing
  Like register
  Update only as clock rises
Rising clock
Register
file
A
B
srcA
valA
srcB
valB
x
2
x
2
y
2
Register
file
W
dstW
valW
Clock
x
2
Register
file
W
dstW
valW
Clock
y
2

## Slide 56: Memory
Memory
  Holds program data and instructions
Ports
  A single address input
  A data input for writing, and a data output for reading
  Error signal means invalid address
Data Memory
address
read
write
Clock
data in
data out
error

## Slide 57: Usage of the Storage Circuits
Clocked Registers
  Hold single words (e.g., PC, CC)
  Loaded as clock rises
Random-access memories
  Hold multiple words (e.g., Register File, Memory)
  Possible multiple read or write ports
  Read word when address input changes
  Write word as clock rises